## Slide 1: Routing in MANET

## Slide 2: Routing Challenges
Packet Routing is much complex task in ad-hoc networks compare to infrastructure based networks.
Topology is keep on changing (Dynamic).
Battery power constraints.
Purpose of Routing:
  To find the best path for destination to deliver the packets from sender.
What we have:
  Traditional routing protocol that is not suitable for ad-hoc’s.
  Each node must have the routing capability to keep the network operational.

## Slide 3: Routing and MANET
MANET Must Concentrate on these:
  Forwarding the packet to the next node (hop).
  While forwarding:
    Ensure that packets moves towards its destination.
    Number of hops/nodes minimized.
    Delay Minimized.
    Packet loss minimized.
    Looping avoided.

## Slide 4: Essentials of Traditional Routing Protocols
Analysis of Traditional (Infrastructure Based) Routing Protocols.
Specific changes need to be done for adapting these for ad-hoc.
Popular protocols.
  Link State Protocols.
  Distance Vector Protocols.
Both are need to compute the shortest path towards destination and forward the packets to next node.
Shortest path is computed according to some specific cost metric such as number of hops in the route.

## Slide 5: Link State Protocols (LSP)
Link State states that connection between neighbour nodes and router.
Every routers has their knowledge about their direct neighbor and flood these information in the network with link state advertisements.
Every routers has their Link State Packet Database (LSPDB) and stores the link state advertisements.
Each router creates the connectivity graph using LSPDB and Dijkstra’s algorithm and finds the shortest path.

## Slide 6: Downside of Link State Protocols (LSP)
LSP’s exchanges a tiny information from each other.
Each node actually constructs the tree using link information local router act as root for the tree.
Then router itself computes the best path to every node from itself.
Frequent hello packets are exchanged to check the connectivity.
No sharing of routing information with it’s neighbor.
LS advertisements are sent whenever the connectivity changes.
LS Advertisement contains only,
  The identity of the router originating the message.
  The identities of all it’s neighbours.

## Slide 7: Distance Vector Protocols
Distance Vectors (DV) stands for routing decisions made based on the distance (number of hops to traverse) to the destination.
Routes are advertised as Vectors (Distance, Direction).
Each node know what is next hop for packet to be forwarded.
DV is based on on the Bellman-Ford algorithm.
It shares everything with its neighbors and computes the topology.
Each router computes the distance based on their perspective and generates the routing table and the table is broadcasted to the neighbors.
Node updates the routing table form the information sent by neighbor and forwards the changes to its neighbors.
This process known as “Routing by Rumour”.

## Slide 8: Downside Distance Vector Protocols
Lack of knowledge about entire path to the destination.
Router believes the information are all valid given by the neighbors it causes the instability.
DV Simply Calculates:
  Direction in (or the specific network interface over) which a packet should be forwarded.
  Its own distance from the destination.
Calculations of Distance done using two protocols
  Routing Information Protocol (RIP). (Node Count) (Cross Platform)
  Interior Gateway Routing Protocol (IGRP). (Node delay and Available Bandwidth) (Cisco Proprietary).

## Slide 9: Routing in MANET vs Traditional Networks
Traditional | MANET
Nodes does not participate in routing. | Every node acts as a router.
Most of the time topology is static. | More dynamic topology.
Routing is easy task because infrequent routing table updates. | Frequent routing table updates required.
Simple IP scheme is enough | Complex schemes takes a part

## Slide 10: Types of Communication
There are 3 types of communication,
  Unicast
    One to One
  Multicast
    One to Group
  Broadcast
    One to All

## Slide 11: Classifications of Unicast MANET Routing Protocols
Unicast MANET Routing Protocols
Proactive (table - driven) protocols
Reactive (on - demand) protocols
Hybrid routing protocols

## Slide 12: Proactive (Table - Driven)
This is table driven protocol.
Each node has the routing table that has the updated information about the routes to all nodes.
Small changes in the network requires routing table updates.
Destination Sequenced Distance Vector Routing Protocol is example of this.
Each nodes knows the complete topology of the networks.
Routing tables needs to be updated periodically.
Lot’s of control messages are sent for route updation.
If mobility of the node is high then this is not the best choice.

## Slide 13: Reactive (On - Demand)
It is on-demand.
Routing table is not updated always.
New routes are discovered and updated only when they actually needed.
Partial route information only available and it uses the flooding technique to discover the routes.
This is designed to reduce the overhead of larger networks.
Highly efficient when the frequent updates are not needed.
Examples:
  Dynamic Source Routing. (DSR)
  Ad-hoc on-demand distance vector routing (AODV)

## Slide 14: Hybrid Routing Protocols
It has the characteristics of both reactive and proactive protocols.
This is designed for achieve scalability and get rid from discovery overheads.
For nearby nodes routes are maintained proactively.
For far nodes routes are maintained reactively.
It is zone based protocol.
Example:
  Zone Routing Protocol.